## Slide 1
Status of R&D on Calorimetry for EIC
EIC R&D Committee Meeting
July 9, 2015
S.Boose, E. Kistenev, J.Haggerty, J.Huang, E.Mannel, C.Pinkenberg,
S. Stoll, and C. Woody
BNL PHENIX Group

## Slide 2: Areas of Investigation
1. Develop techniques for producing tungsten powder epoxy
scintillating fiber modules for a central barrel EMCAL
  Produce 1D tapered modules (similar to the ones produced at UCLA) at several locations in order to understand and develop the fabrication techniques
    BNL
    University of Illinois Urbana Champaign
    Tungsten Heavy Powder
  Develop techniques suitable for mass production
  Develop 2D tapered modules as required for a fully projective barrel calorimeter as needed by sPHENIX
2. Study radiation damage in SiPMs
  Irradiate SiPMs in the PHENIX IR
    Measure increase in dark current with dose
    Determine if any damage is caused by thermal neutrons
    Determine if any damage is caused by spallation neutrons
  Measure effects of neutron damage at very high doses

## Slide 3: W/SciFi Module Production at BNL
Single Tapered Modules
Five single tapered modules have been produced at BNL
Overall quality looks good (density, uniformity, light transmission of fibers,…)
Few remaining issues (small bubbles, inclusions, encroachment of W powder into clear epoxy,…)
Note: This was mainly a learning exercise in order to become familiar with the construction
technique which will then be used to build fully projective modules

## Slide 4: W/SciFi Module Production at BNL
Preparations to Construct Double Tapered Modules
3D Model
Fibers stacked in tapered hole meshes
Meshes filled with fibers using hopper
Fiber assemblies in molds 

## Slide 5: W/SciFi Module Production at UIUC
Fiber ends are smooth and clear
Cutting and polishing ends of module with diamond fly cutter
V. Loggins, E. Thorsland and A. Sickles

## Slide 6: W/SciFi Module Production at THP
Process uses a somewhat different technique than developed by UCLA
After impregnating both ends with clear epoxy, mold is partially filled with clear epoxy
Tungsten powder is added on top of clear epoxy
Mold is centrifuged to compact powder into epoxy
Process is repeated 3 times to fill the mold

## Slide 7: SiPMs Irradiated in the PHENIX IR
Six Hamamatsu S12572-015P 15 mm micropixel SiPMs were placed in the PHENIX IR during the last RHIC run.
Channels 1&2 were enclosed in a Gd box that absorbed all thermal neutrons.
Channels 3&4 were unshielded in the same location.
Channels 5&6 were also unshielded and located at the base of the central magnet next to a W/Scifi SPACAL block.
Conclusion: No effect on damage due to either thermal neutrons or spallation neutrons

## Slide 8: SiPMs Irradiated to High Neutron Fluences
Increase in noise for a group of Hamamatsu S12572-025P SiPMs exposed to various levels of neutron fluence at the LENS facility at the Indiana University Cyclotron

## Slide 9
Future Plans
W/SciFi module production
  Continue to develop the procedure to build fully projective spacal modules using similar techniques that were used to produce single projective modules. This will be done primarily at BNL and UIUC and will be funded by sPHENIX R&D funds.
  Continue to develop procedures for mass production of spacal modules using the standard 1D projective design. This will be done primarily at THP, but improvements to the process will also be developed at UCLA, BNL and UIUC.
  Construct an 8x8 prototype calorimeter using single tapered modules produced at THP using their mass production method. This prototype will then be tested as part of a beam test of the sPHENIX calorimeter systems at Fermilab in the spring of 2016.
  In parallel, we plan to transfer the technology for producing double tapered modules to THP and adapt this procedure to their mass production process. We will then ask them to produce a second 8x8 array of modules that will be used to construct a second prototype that will be tested at Fermilab later in 2016.

## Slide 10
Future Plans
Studies on radiation damage in SiPMs
  Carry out additional tests of SiPMs with MeV equivalent neutrons to study the increase in dark current with dose and determine if there is any effect on the PDE at higher doses
  Develop the electronics and control procedures to stabilize the gain of the SiPMs with temperature and with increasing dark current due to radiation exposure. This will involve studies of both electronic control systems as well as cooling and temperature control.